Technique Risk Assessment

| Ethidium Bromide gels |
| --- |
| Department: NDM Location of work: NDM Research Building First Floor | Persons involved: Borrow Group Dorrell Group McMichael Group Rowland-Jones Group |
| Risk matrix | Likelihood |
|  | High | Medium | Low | Negligible |
| Consequence | Severe | High | High | Medium | Effectively Zero |
|  | Moderate | High | Medium | Medium/Low | Effectively Zero |
|  | Insignificant | Medium/Low | Low | Low | Effectively Zero |
|  | Negligible | Effectively Zero | Effectively Zero | Effectively Zero | Effectively Zero |
| Overall risk of this technique: Low |
| Substances used | Quantities used | Frequency of use | Hazards identified | Exposure route |
| Ethidium Bromide | 2.5ul per 50ml of gel (20mg/ml) | Weekly/ as required | Toxic Health Hazard | In contact with Skin or eye, Ingestion |
| UV light | Generated by equipment |  | Harmful | Contact with eyes. |
| GHS statements: Ethidium Bromide: H331 Toxic if inhaled. H341 Suspected of causing genetic defects. UV Risk of accidental UV exposure |
| Could a less hazardous substance (or form of the substance) be used instead? Yes |
| Justify not using it: The sensitivity of Ethidium Bromide has not been equalled by the other products tested so far. |
| Safe work practices: Universal precautions for working at containment level 2; GLP and adherence to laboratory rules. Avoid the use of sharps. |
| Engineering controls: Interlock system on the Gel Doc system – UV will turn itself automatically if the door is opened. |
| Personal Protective Equipment: Disposable nitrile gloves Laboratory coat Safety glasses. |
| Management measures: Small scale use; work will be undertaken by researchers only and inexperienced researchers will be supervised/given on the job training. |
| Checks on control measures: |
| Is health surveillance required? No | Training requirements: General training for containment level 2 |
| Emergency procedures: Out of hours emergencies, contact University Security Services on (2)89 999. Report accident to DSO (ling Jinks) as soon as possible. | Waste disposal: Follow NDMRB-SOP-003 for disposal of lab waste: Clinical waste to be incinerated. Liquid waste to be treated with 1% Virkon for at least 30min. Solid waste to be autoclaved. |
| Name and position of assessor: Tiphaine Bouriez-Jones Laboratory Manager | Date: 12/01/2015 |