Technique Risk Assessment

| Preparation and running of samples for FACS analysis |
| --- |
| Department: NDM Location of work: NDM Research Building First Floor | Persons involved: Bafadhel Borrow Group Dorrell Group Ho Group McMichael Group Pavord Group Rowland-Jones Group Xue Group |
| Risk matrix | Likelihood |
|  | High | Medium | Low | Negligible |
| Consequence | Severe | High | High | Medium | Effectively Zero |
|  | Moderate | High | Medium | Medium/Low | Effectively Zero |
|  | Insignificant | Medium/Low | Low | Low | Effectively Zero |
|  | Negligible | Effectively Zero | Effectively Zero | Effectively Zero | Effectively Zero |
| Overall risk of this technique: Medium |
| Substances used | Quantities used | Frequency of use | Hazards identified | Exposure route |
| Human Cells | Max 1 x 107 cells in 10 mL media | Weekly/ as required | Potentially infectious | In contact with Skin or eye, Ingestion |
| Paraformaldehyde (PFA) | Up to 200ul at 4% per sample |  | Health Hazard, Harmful, Corrosive, Flammable | Inhalation, Contact with Skin or eye, Ingestion |
| Sheath Fluid/waste tank | 20L tank |  | Manual Handling Operation |
| Trypan Blue | Max 1 ml per count |  | Health Hazard | In contact with Skin or eye, Ingestion |
| Virkon | Powdered form, used at 1% in solution |  | Corrosive Harmful/Irritant Dangerous for the environment | Inhalation, contact with skin and eyes, ingestion. |
| GHS statements: Human Cells: Potential biohazard – see specific biological risk assessment if appropriate Industrial Methylated Spirit (IMS): H225 Highly flammable liquid and vapour. H302 Harmful if swallowed. paraformaldehyde: H228 Flammable solid. H302 + H332 Harmful if swallowed or if inhaled H315 Causes skin irritation. H317 May cause an allergic skin reaction. H318 Causes serious eye damage. H332 Harmful if inhaled. H335 May cause respiratory irritation. H335 May cause respiratory irritation. H351 Suspected of causing cancer. Trypan Blue: H350 May cause cancer. Virkon H314 Causes severe skin burns and eye damage. H302 Harmful if swallowed. H410 Very toxic to aquatic life with long lasting effects. |
| Could a less hazardous substance (or form of the substance) be used instead? No |
| Justify not using it: |
| Safe work practices: Universal precautions for working at containment level 2/3; GLP and adherence to laboratory rules. Avoid the use of sharps. Waste should be emptied before it is full to avoid lifting heavy weight. |
| Engineering controls: Use of Biological Safety Cabinets whilst handling the cells. Trolley available to move the sheath fluid tank to the FACS machine. |
| Personal Protective Equipment: Disposable nitrile gloves – double gloving if working in Cat3. Laboratory coat – disposable reinforced disposable labcoat if working in Cat3. Safety glasses. |
| Management measures: Small scale use; work will be undertaken by researchers only and inexperienced researchers will be supervised/given on the job training. |
| Checks on control measures: BSC serviced and validated annually (CL2) or bi-annually (CL3) Trolley is visually inspected for defect on a regular basis. |
| Is health surveillance required? No | Training requirements: General training for containment level 2/3 |
| Emergency procedures: Spills of biological material: Aerosols should be allowed to settle, then wearing protective clothing, the spill should be covered with absorbent paper towel and a 0.01-5% Virkon solution should be applied (starting at the perimeter and working towards the centre) and left for 30min. Exposure to biological material: remove gloves, irrigate eye with eyewash solution, rinse mouth/nose with water. Wash skin gently with soap and water. Out of hours emergencies, contact John Warin Ward on 01865 225214 (Infectious diseases and tropical medicine) or University Security Services on (2)89 999. Report accident to DSO (ling Jinks) as soon as possible. | Waste disposal: Follow NDMRB-SOP-003 for disposal of lab waste: Clinical waste to be incinerated. Liquid waste to be treated with 1% Virkon for at least 30min. Solid waste to be autoclaved. |
| Name and position of assessor: Tiphaine Bouriez-Jones Laboratory Manager | Date: 08/01/2015 |